## Slide 1
PLANETSORT: ORBITQUEST
Advanced Interactive Mechatronic Product Design System
ARES SECTOR
RED ORBIT
GAEA SECTOR
GREEN ORBIT
Ziad Atef M. Riad
24P0103
Kamal Wahdan
24P0222
Zeyad Amr Nazih
24P0372
Yahya Ashraf
24P0370
Abdoulrahman Adel
24P0098
Ain Shams University · University of East London · Project Defense 2026

## Slide 2
PHASE I: VISION
Designing an autonomous, space-themed
planetary sorting and launching system
focused on cognitive development and STEM engagement.
Real project prototype — assembled for defense

## Slide 3
User Research & Target Persona
Primary Audience
Children aged 2–10 years. Focused research indicates high engagement for age 8 through visually stimulating mechanical feedback and goal-oriented tasks.
Core Needs
Visual stimulation (moving parts), color recognition, hand-eye coordination, and a safe, intuitive interface for 'closed-loop' play.
2–10
Target Age Range
3
Core Modules
100×100
cm Footprint

## Slide 4
The Design Challenge
Automated Sorting
Autonomous color detection and path routing using optical sensing logic.
Vertical Lifting
Continuous vertical transit via an Archimedes spiral mechanism.
Orbital Launch
High-velocity calibrated projection into a target basketball hoop.

## Slide 5
Module I: PlanetScan Sorting
The sorting subsystem identifies planetary marbles by wavelength using the TCS3200 sensor array. Dual SG90 micro-servos actuate high-speed gates to route the spheres.
Real-time RGB frequency analysis
Non-contact optical gating
Dynamic error-correction routing

## Slide 6
Module II: Orbital Elevator
Our lifting mechanism utilizes a NEMA 17 stepper motor to drive a 3D-printed helical flight screw within a smooth-walled cylinder.
This module provides precise vertical positioning for the launch bay, ensuring the system is ready for the high-velocity shooting phase.
Motor:
NEMA 17 Stepper
Mechanism:
Archimedes Spiral
Material:
3D-Printed PLA

## Slide 7
Module III: Hyperspace Thruster
The shooting module utilizes twin counter-rotating friction wheels driven by high-RPM DC motors. Calibration ensures repeatable orbital injection.
By modulating the PWM duty cycle, we achieve the precise initial velocity required to overcome gravity and reach the target hoop.
4.15 m/s
Calibrated Launch Velocity · β = 30°

## Slide 8
Master-Slave Control Logic
ESP32 Master
Handles high-level tasks: Color sensing, TFT display, Bluetooth telemetry, and ESP-NOW communication with the slave controller.
Arduino Uno Slave
Dedicated to low-level actuation: Precise stepper pulses, DC motor PWM curves, and servo timing isolation.
Communication via ESP-NOW wireless protocol · 2.4 GHz band

## Slide 9
Dual Interfaces: Mission Control
LCD Control Panel
Local onboard display · Colour detection readout
Green & Red button input
Ball Sorter App
Bluetooth remote control · Score tracking
Shoot speed slider · RGB sensor raw data

## Slide 10
Engineering Validation
Parameter | Value | Validation Status
Initial Velocity (v₀) | 4.15 m/s | Calculated & Tested
Launch Angle (β) | 30° | Fixed Mechanical Constraint
Current Draw (Max) | < 5.0 A | Fused Safety Limit
Motor Safety Factor | > 2.2 | Industry Standard Compliant

## Slide 11
Safety & Compliance Protocols
Concealed Architecture
All electrical wiring routed through internal structural channels to remain completely hidden and safe.
Thermal Safety
Onboard resettable 5A PTC fuse safeguards logic and motor rails against stall-current overloads and overheating.
Child-Safe Materials
Non-toxic PLA and smoothed MDF surfaces eliminate sharp edges and chemical exposure risks.
Hardware Interrupt
A physical master-stop button provides immediate electrical isolation of all high-power actuators.
OrbitQuest: Launching Curiosity into STEM · Ain Shams University & University of East London · Project Defense 2026